# GENERATOR FLASHLIGHT MAGNIFIER

- 3 super-bright LEDS

- Used for auto, family, camping and when power failure

- Always work (without battery).

# ILLUMINATIVE TIME

- Rotate the handle for 1 min. ≥ 25mins.

- Power switch (1)

- 1 X = 3 LEDs on

- 2 X = 3 LEDs off

# Mobile phone charging

Turning handle three minutes, will enable mobile phone calls 2-8 minutes

# CHARGING

- Turn off the light (1)

- Reverse the crank (2)

- Rotate the handle (3) according to the direction of arrow.

- Reverse the crank back.

Magnifying times: Twice and 8 times

# ATTENTIONS

- Turn off it when no use

- Turn off it when charging.

- Only rotate it in one direction for charging.

- Don’t directly shine eyes.

- Prevent it from water spray and don’t soak it into water.